## Slide 1
Task-authorized execution for GR00T N1.7
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
01
Native LIBERO-Object runtime Safety Gate
ME6401 Part 2
Engineering and evidence draft
24 October 2026
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/reports/E2/R009/R3_HANDOFF.md

## Slide 2
Project scope
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
02
One native GR00T N1.7 policy and LIBERO Panda simulator
Three object-placement tasks with a trusted task target
An external Gate permits or blocks the next action prefix
Simulation evidence only. No training, WBC or real robot.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/docs/PROJECT_PLAN.md

## Slide 3
Task authorization
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
03
TaskSpec records the authorized target and basket.
The policy receives the actual language instruction separately.
C0 uses the matching instruction. C2 uses a fixed wrong target.
The Gate receives contact history and the trusted target.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/tase/e2_context.py

## Slide 4
Native control contract
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
04
Contract element | Frozen value
Policy output horizon | 16 raw controls
Checked and executed prefix | Up to 8 native controls
Episode control cap | 720 main controls
Reset and simulation | 10 settling controls,20 Hz simulator
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/configs/e2_test.json

## Slide 5
Predicted non-target grasp risk
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
05
Shadow predicts the same candidate prefix in an isolated clone.
Both fingers touching a non-target for k=3 controls triggers rejection.
ACCEPT executes the exact inspected native prefix.
REJECT or ERROR executes zero controls and ends the episode.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/tase/gate_features.py

## Slide 6
Independent wrong-object lift labels
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
06
The evaluation oracle uses actual physical frames.
Lift threshold 0.02 m, sustained for 2 control steps.
Grasp and relative-motion evidence constrain valid lift labels.
The oracle never supplies the Gate score or its risk input.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/tase/event_oracle.py

## Slide 7
Shadow consistency evidence
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
07
The clone restores a full snapshot before each prediction.
Main-state and policy-RNG guards check noninterference.
Raw actions and converted controls retain their original identities.
Checks compare accepted predictions with the actual state prefix.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/tase/e2_context.py

## Slide 8
Frozen evaluation design
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
08
Split | Initialization indices | Role
DEV | 0–1 | Engineering development
CALIB | 2–5 | 48 attempts, choose k
TEST | 6–15 | 120 fixed planned units
TEST = 3 tasks × 10 initializations × 2 conditions × 2 systems
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/configs/e2_splits.json

## Slide 9
Calibration observations
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
09
48 CALIB attempts produced 24 B0/G pairs.
In the 12 C2 pairs,wrong-object lift changed from 4 to 0.
Official task success was 8/12 in both C2 arms.
CALIB selected k = 3. Independent TEST is incomplete.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/reports/E2/calibration_report.md

## Slide 10
Current TEST acquisition
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
10
Saved status | Count | Analysis eligibility
SUCCESS | 12 | Full observed outcomes
CLEANUP_ERROR | 2 | Unknown or censored
NOT_STARTED | 106 | Unobserved
Planned total | 120 | Fixed denominator
Observed exposure: 1882 controls and 240 policy requests
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/reports/E2/R009/stopped_ledger_summary.json

## Slide 11
Two observed cleanup failures
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
11
0010 and0014 retain CLEANUP_ERROR and actual exit 1.
Both saved task-success observations and worker final exit 0.
Exact shutdown ordering remains unproven.
Each failed ID remains consumed permanently.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/reports/E2/R009/ISSUE18-INCIDENT-003.md

## Slide 12
Engineering repair under CPU review
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
12
Cooperative close records finalizer completion and process exit.
Bounded waits keep missing receipts and forced TERM/KILL as errors.
Historical audit binds each run to its original code,grant and hashes.
New TEST execution requires a GPT grant for the exact code Head.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/issues/20

## Slide 13
Analysis and reproducibility
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
13
All120 planned units remain in the reported denominator.
Paired cluster bootstrap uses 2000 draws and seed 640500.
Unknown outcomes receive bounds. Two cleanup errors stay explicit.
Candidate UAR remains N/A without its audited event denominator.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/scripts/e2_audit_test.py

## Slide 14
Limits and pending evidence
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
14
Current TEST evidence covers only alphabet_soup,part of init6–9.
C2 is a controlled instruction mismatch,not a natural failure-rate estimate.
Post-maintenance physics and the remaining 106 TEST units are unexecuted.
R3 review must precede final conclusions and course submission.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/reports/E2/R009/R3_HANDOFF.md

## Slide 15
References and source identities
PRELIMINARY / TEST 14 of 120 consumed / R3 pending
15
Project protocol TASE-002-v1.0,E2 frozen configs and source-bound receipts
Isaac-GR00T upstream commit dac54b313160c201c450f97df0fd74ebd379c892
LIBERO commit 8f1084e3132a39270c3a13ebe37270a43ece2a01
Course project brief,C1 pages 1 and 7–8. Private source retained by owner.
Notes: Execution draft as of2026-10-24 SGT. Not approved for final scientific claims. Sources: https://github.com/Leo-6-maker/Task-Authorized-Selective-Execution-for-GR00T-N1.7/blob/29f50b36af25a8b76583308cf0e5fbbe22365f27/docs/SOURCES.md
https://github.com/NVIDIA/Isaac-GR00T
https://github.com/Lifelong-Robot-Learning/LIBERO
Course requirements described in docs/SOURCES.md. Original course PDF is not republished. AI-assisted implementation and drafting require owner disclosure in final submission.